## Slide 1: Norma universal firmware introduction

## Slide 2: System & SKU List
System Name | Sku Number | SKU ID (Byte 1) | System ID (Byte 0) | Note
CB502-NM | SKU 1 | 0x01 | 0x01 | 4xNVME

## Slide 3: Important Notes
If you changed the System ID & SKU ID , you must reboot to update the boot setting.

## Slide 4: How to modify different system & sku
ipmitool -I lanplus -H “your ip” -U “username” -P “password” raw 0x3A 0xA0
This command can get the current system id & sku id in first and second byte(01 02).

## Slide 5: How to modify different system & sku
ipmitool -I lanplus -H “your ip” -U “username” -P “password” raw 0x3A 0xA1 “system id” “sku id”
This command can set system id & sku id.
ipmitool -I lanplus -H “your ip” -U “username” -P “password” raw 0x00 0x02 0x02
When set completed, must enter the command to power cycle.

## Slide 6: How to modify different system & sku
Before power cycling, you can confirm if system id and sku id were modified.

## Slide 7: How to modify different system & sku
If you want to modify BIOS setting and power cycle at the same time, press “Save Changes” then enter the command on page 4 to power cycle(0x00 0x02 0x02).

## Slide 8: End